## Slide 1
Engineering Design of a Manually Actuated Lead-Screw Scissor Lift
Agenda
This presentation aims to outline the design and fabrication of a manual lead-screw-driven scissor lift by combining strong mechanical design methods with accurate modeling and material-based performance assessment.

## Slide 2
Team members
Mohammad Arshad
Mohit Raj Sutrave
Mohammed Khaja Ahmed
Agenda
This presentation aims to outline the design and fabrication of a manual lead-screw-driven scissor lift by combining strong mechanical design methods with accurate modeling and material-based performance assessment.

## Slide 3
Agenda
This presentation aims to outline the design and fabrication of a manual lead-screw-driven scissor lift by combining strong mechanical design methods with accurate modeling and material-based performance assessment.
5
Conclusion
4
Calculations
3
Modeling and Assembly
2
Design Considerations
1
Project Overview & Problem Statement
FIVE
STEPS

## Slide 4
Agenda
This presentation aims to outline the design and fabrication of a manual lead-screw-driven scissor lift by combining strong mechanical design methods with accurate modeling and material-based performance assessment.
FIVE
STEPS
5
Conclusion
4
Calculations
3
Modeling and Assembly
2
Design Considerations
1
Project Overview & Problem Statement

## Slide 5
FIVE
STEPS
Project Overview & Problem Statement
5
Conclusion
4
Calculations
3
Modeling and Assembly
2
Design Considerations
1
Project Overview & Problem Statement

## Slide 6
Project Overview & Problem Statement

## Slide 7
Project Overview & Problem Statement

## Slide 8
Design Considerations

## Slide 9
Design Considerations

## Slide 10
Modeling and assembly
Here are the CAD-modeled components that form the complete scissor lift mechanism.
These visuals help in understanding the structure, assembly process, and functional layout.
Function
Provides stable top support for load distribution by offering a rigid mounting interface for components
Material Selection
AISI 1020
Chosen for its good strength and excellent machinability.
Base Top

## Slide 11
Function
Provides stable top support for load distribution by offering a rigid mounting interface for components
Material Selection
AISI 1020
Chosen for its good strength and excellent machinability.
Base Top
Modeling and assembly
Here are the CAD-modeled components that form the complete scissor lift mechanism.
These visuals help in understanding the structure, assembly process, and functional layout.
Function
Converts rotational motion into linear lifting action delivering smooth and controlled vertical displacement of the scissor mechanism.
Material Selection
AISI 4340 Steel, annealed
Selected for its high toughness and superior strength ideal for load-bearing shaft applications.
Lead Screw

## Slide 12
Function
Converts rotational motion into linear lifting action delivering smooth and controlled vertical displacement of the scissor mechanism.
Material Selection
AISI 4340 Steel, annealed
Selected for its high toughness and superior strength ideal for load-bearing shaft applications.
Lead Screw
Function
Supports the scissor mechanism vertically by providing structural stability while resisting bending and operational stresses.
Material Selection
ASTM A36 steel
Selected for its high structural strength and good weldability.
Leg Support
Function
Provides stable top support for load distribution by offering a rigid mounting interface for components
Material Selection
AISI 1020
Chosen for its good strength and excellent machinability.
Base Top

## Slide 13
Function
Supports the scissor mechanism vertically by providing structural stability while resisting bending and operational stresses.
Material Selection
ASTM A36 steel
Selected for its high structural strength and good weldability.
Leg Support
Function
Holds and guides the lead screw securely maintaining smooth rotational movement of the shaft.
Material Selection
Phosphor Bronze 10% D (UNS C52400)
Chosen for its excellent wear resistance and low friction properties.
Cylindrical Support
Function
Converts rotational motion into linear lifting action delivering smooth and controlled vertical displacement of the scissor mechanism.
Material Selection
AISI 4340 Steel, annealed
Selected for its high toughness and superior strength ideal for load-bearing shaft applications.
Lead Screw

## Slide 14
Function
Holds and guides the lead screw securely maintaining smooth rotational movement of the shaft.
Material Selection
Phosphor Bronze 10% D (UNS C52400)
Chosen for its excellent wear resistance and low friction properties.
Cylindrical Support
Function
Supports the scissor mechanism vertically by providing structural stability while resisting bending and operational stresses.
Material Selection
ASTM A36 steel
Selected for its high structural strength and good weldability.
Leg Support
Function
Restricts axial movement between the support and lead screw while permitting free rotation ensuring stable transmission of motion and maintaining alignment under load.
Material Selection
Phosphor Bronze 10% D (UNS C52400)
Chosen for its excellent wear resistance and low friction properties.
Cylindrical Support Fixed

## Slide 15
Function
Restricts axial movement between the support and lead screw while permitting free rotation ensuring stable transmission of motion and maintaining alignment under load.
Material Selection
Phosphor Bronze 10% D (UNS C52400)
Chosen for its excellent wear resistance and low friction properties.
Cylindrical Support Fixed
Function
Holds and guides the lead screw securely maintaining smooth rotational movement of the shaft.
Material Selection
Phosphor Bronze 10% D (UNS C52400)
Chosen for its excellent wear resistance and low friction properties.
Cylindrical Support
Function
Acts as a point joint connecting the scissor leg supports enabling smooth pivoting motion and stable load transfer during operation.
Material Selection
Alloy Steel (SS)
Chosen for its high strength and wear resistance.
Pin

## Slide 16
Function
Acts as a point joint connecting the scissor leg supports enabling smooth pivoting motion and stable load transfer during operation.
Material Selection
Alloy Steel (SS)
Chosen for its high strength and wear resistance.
Pin
Function
Restricts axial movement between the support and lead screw while permitting free rotation ensuring stable transmission of motion and maintaining alignment under load.
Material Selection
Phosphor Bronze 10% D (UNS C52400)
Chosen for its excellent wear resistance and low friction properties.
Cylindrical Support Fixed
Function
Provides a stable interface between the scissor leg support and base plate allowing smooth rotation
Material Selection
Cast Alloy Steel
Selected for its durability and ability to withstand cyclic loads.
Bush

## Slide 17
Function
Provides a stable interface between the scissor leg support and base plate allowing smooth rotation
Material Selection
Cast Alloy Steel
Selected for its durability and ability to withstand cyclic loads.
Bush
Function
Acts as a point joint connecting the scissor leg supports enabling smooth pivoting motion and stable load transfer during operation.
Material Selection
Alloy Steel (SS)
Chosen for its high strength and wear resistance.
Pin
Function
Secures axial position between the lead screw and cylindrical support preventing unwanted movement while allowing smooth rotational action.
Material Selection
AISI 1020
Chosen for its strength and reliable performance in retaining applications.
Circlip

## Slide 18
Function
Secures axial position between the lead screw and cylindrical support preventing unwanted movement while allowing smooth rotational action.
Material Selection
AISI 1020
Chosen for its strength and reliable performance in retaining applications.
Circlip
Function
Provides a stable interface between the scissor leg support and base plate allowing smooth rotation
Material Selection
Cast Alloy Steel
Selected for its durability and ability to withstand cyclic loads.
Bush
The assembly integrates all components into a coordinated scissor-lift mechanism that converts rotational input into stable vertical motion. Each part is fitted with precise clearances and selected materials to ensure smooth operation, structural reliability, and long-term durability.
Assembly

## Slide 19
The assembly integrates all components into a coordinated scissor-lift mechanism that converts rotational input into stable vertical motion. Each part is fitted with precise clearances and selected materials to ensure smooth operation, structural reliability, and long-term durability.
Assembly
Function
Secures axial position between the lead screw and cylindrical support preventing unwanted movement while allowing smooth rotational action.
Material Selection
AISI 1020
Chosen for its strength and reliable performance in retaining applications.
Circlip

## Slide 20
CALCULATIONs

## Slide 21
CALCULATIONs

## Slide 22
CALCULATIONs

## Slide 23
FEA

## Slide 24
FEA

## Slide 25
Conclusion